## Slide 1
Speech Recognizer
Building a voice command classifier from scratch
Machine Learning · Audio Processing · Python

## Slide 2
What is this project?
🎤
Voice Input
Records or loads audio of spoken sentences and converts them to WAV format for processing.
📊
Feature Extraction
Extracts MFCC features (120 dimensions) from each audio clip to represent the sound mathematically.
🤖
Classification
Trains a Random Forest model to recognize which sentence was spoken from the features.

## Slide 3
Dataset
How the data
was built
101
Sentences
1,200
Audio samples
5
Speaking speeds
120
MFCC features
Text-to-Speech Generation
Each of the 101 command sentences was synthesized using the espeak TTS engine at 5 different speaking speeds — slow, medium, normal, medium-fast, and fast. This gave us consistent coverage across all sentence classes.
Example sentences:
"Turn on the lights"
"What is the weather today"
"Set a timer for 5 minutes"
"Play some music"

## Slide 4
Making It Realistic
Without augmentation, TTS audio gives 100% accuracy — a misleading result. These techniques force the model to generalize.
🔇 Clean
No changes — baseline
📢 Noisy
White noise added (10–20 dB SNR)
⏩ Stretched
Speed variation ±15%
🎵 Pitched
Pitch shifted ±3 semitones
🌀 Noisy + Pitched
Combined: noise and pitch

## Slide 5
Feature Extraction
What are MFCCs?
Mel-Frequency Cepstral Coefficients (MFCCs) mimic how the human ear perceives sound. They compress audio into a compact set of numbers that capture the key characteristics of speech — much better than raw waveforms.
What we extract per clip:
40 MFCC mean values
40 MFCC standard deviations
40 Delta MFCC means
Audio WAV
↓
MFCC (40)
↓
Delta MFCC
↓
120-dim vector
↓
Classifier

## Slide 6
The Model
Random Forest Classifier
300
Trees
None
Max Depth
2
Min Samples Split
75% / 25%
Train / Test Split
Yes
Stratified

## Slide 7
Why 100% Accuracy Is Not Real
🤖 Synthetic Audio
All audio was generated by the same TTS engine (espeak). The model memorizes the robot voice, not real speech patterns.
🔁 Data Leakage
Train and test sets come from the same generator with the same settings — there is no true unseen data.
🎙️ Real Test
When you record your own voice, accuracy drops to 10–40%. That is the honest number for a prototype.
✅ The Fix
Augmentation (noise, pitch, speed) was added to force the model to generalize, bringing accuracy to a realistic 60–85%.

## Slide 8
Testing With Your Own Voice
1
Record a sentence
Say one of the 101 training sentences out loud, e.g. "turn on the lights".
2
Save as WAV
Use 16 kHz mono. Any phone recorder or Audacity works fine.
3
Upload to Kaggle
Click + Add Input → Upload → New Dataset and upload your WAV file.
4
Run recognition
Set MY_AUDIO = "/kaggle/input/your-dataset/your-file.wav" in Cell 10, then run.

## Slide 9
Limitations & Future Work
Current Limitations
Possible Improvements
Closed vocabulary — only 101 sentences
Synthetic training data, not real voices
Background noise hurts accuracy
Single language (English) only
Record real human voice datasets
Use deep learning (CNN/RNN) models
Add noise robustness in pipeline
Expand to multilingual commands

## Slide 10
Key Takeaways
1
Built an end-to-end speech classifier using MFCC features and Random Forest
2
Synthetic data alone gives misleading accuracy — augmentation is essential
3
Real-world performance depends on using real voices in training
4
A solid foundation to build on with deep learning and larger datasets